## Slide 1
O‘QUV TAQDIMOTI
Robotlarning diskret pozitsion
dasturiy boshqaruv tizimlari
Robotlarning dasturiy boshqaruv tizimlari
01 / 15
Robot belgilangan nuqtalarga qanday harakat qiladi?
DASTUR
BOSHQARUVCHI
ROBOT
Dasturdagi har bir nuqta ish siklining bir bosqichini belgilaydi
Notes: O‘quv taqdimoti. Chizmalar mavzuni tushuntirish uchun soddalashtirilgan. Manbalar: https://modernrobotics.northwestern.edu/nu-gm-book-resource/9-1-and-9-2-point-to-point-trajectories-part-1-of-2/
https://www.universal-robots.com/manuals/EN/HTML/SW10_10/Content/prod-scriptmanual/all_scripts/movej_qa14v105t0r.htm
https://www.universal-robots.com/manuals/EN/HTML/SW5_19/Content/prod-usr-man/complianceUR16e/SW_sections/first_program/move.htm

## Slide 2
MAVZU TARKIBI
Taqdimot rejasi
Robotlarning dasturiy boshqaruv tizimlari
02 / 15
01
Asosiy tushunchalar
Diskret, pozitsion va kontur boshqaruvi
02
Tizimning tuzilishi
Kontroller, yuritma va teskari aloqa
03
Harakatni boshqarish
Pozitsiyalar va tezlik profili
04
Amaliy ish sikli
Detalni olish, ko‘chirish va qo‘yish
05
Sozlash va baholash
Dasturlash, afzalliklar va cheklovlar
Notes: O‘quv taqdimoti. Chizmalar mavzuni tushuntirish uchun soddalashtirilgan. Manbalar: https://modernrobotics.northwestern.edu/nu-gm-book-resource/9-1-and-9-2-point-to-point-trajectories-part-1-of-2/
https://www.universal-robots.com/manuals/EN/HTML/SW10_10/Content/prod-scriptmanual/all_scripts/movej_qa14v105t0r.htm
https://www.universal-robots.com/manuals/EN/HTML/SW5_19/Content/prod-usr-man/complianceUR16e/SW_sections/first_program/move.htm

## Slide 3
ROBOTOTEXNIKA / POZITSION BOSHQARUV
Asosiy tushuncha
Robotlarning dasturiy boshqaruv tizimlari
03 / 15
01
Robot dasturda ko‘rsatilgan nuqtalarga navbat bilan boradi.
02
Keyingi amal robot kerakli joyga yetgach yoki berilgan shart bajarilgach boshlanadi.
03
“Diskret” so‘zi ish jarayoni alohida bosqichlardan tuzilishini bildiradi.
P1
P2
P3
Pozitsiyalar orasida robot
uzluksiz harakat qiladi.
Notes: O‘quv taqdimoti. Chizmalar mavzuni tushuntirish uchun soddalashtirilgan. Manbalar: https://modernrobotics.northwestern.edu/nu-gm-book-resource/9-1-and-9-2-point-to-point-trajectories-part-1-of-2/
https://www.universal-robots.com/manuals/EN/HTML/SW10_10/Content/prod-scriptmanual/all_scripts/movej_qa14v105t0r.htm
https://www.universal-robots.com/manuals/EN/HTML/SW5_19/Content/prod-usr-man/complianceUR16e/SW_sections/first_program/move.htm

## Slide 4
ROBOTOTEXNIKA / POZITSION BOSHQARUV
Boshqaruv turlarining farqi
Robotlarning dasturiy boshqaruv tizimlari
04 / 15
Siklli boshqaruv
Mexanizm oldindan belgilangan chekka holatlar orasida ishlaydi.
Misol: silindrni uzaytirish va qaytarish.
Pozitsion boshqaruv
Robot dasturda saqlangan nuqtalarga navbat bilan boradi.
Misol: detalni bir joydan boshqa joyga ko‘chirish.
Kontur boshqaruvi
Asbobning harakati butun yo‘l bo‘ylab boshqariladi.
Misol: yoy bo‘ylab chok hosil qilish.
Pozitsion boshqaruvda asosiy talab robotning belgilangan nuqtaga yetishidir.
Notes: O‘quv taqdimoti. Chizmalar mavzuni tushuntirish uchun soddalashtirilgan. Manbalar: https://modernrobotics.northwestern.edu/nu-gm-book-resource/9-1-and-9-2-point-to-point-trajectories-part-1-of-2/
https://www.universal-robots.com/manuals/EN/HTML/SW10_10/Content/prod-scriptmanual/all_scripts/movej_qa14v105t0r.htm
https://www.universal-robots.com/manuals/EN/HTML/SW5_19/Content/prod-usr-man/complianceUR16e/SW_sections/first_program/move.htm

## Slide 5
ROBOTOTEXNIKA / POZITSION BOSHQARUV
Boshqaruv tizimi qanday tuzilgan?
Robotlarning dasturiy boshqaruv tizimlari
05 / 15
Dastur
xotirasi
Kontroller
Yuritma
Manipulator
Holat datchiklari
Teskari aloqa
Operator pulti orqali nuqtalar yoziladi, dastur tanlanadi va robot holati kuzatiladi.
Notes: O‘quv taqdimoti. Chizmalar mavzuni tushuntirish uchun soddalashtirilgan. Manbalar: https://modernrobotics.northwestern.edu/nu-gm-book-resource/9-1-and-9-2-point-to-point-trajectories-part-1-of-2/
https://www.universal-robots.com/manuals/EN/HTML/SW10_10/Content/prod-scriptmanual/all_scripts/movej_qa14v105t0r.htm
https://www.universal-robots.com/manuals/EN/HTML/SW5_19/Content/prod-usr-man/complianceUR16e/SW_sections/first_program/move.htm

## Slide 6
ROBOTOTEXNIKA / POZITSION BOSHQARUV
Pozitsiya qanday ifodalanadi?
Robotlarning dasturiy boshqaruv tizimlari
06 / 15
Bo‘g‘im koordinatalari
q = [q₁, q₂, …, qₙ]
Aylanuvchi bo‘g‘im: burchak
Ilgarilanma bo‘g‘im: siljish
Ishchi organ holati
P = (x, y, z, orientatsiya)
Dekart koordinatalari va asbob yo‘nalishi robotning ish fazosidagi holatini belgilaydi.
Teskari kinematika berilgan asbob holatidan bo‘g‘im koordinatalarini topadi.
Notes: O‘quv taqdimoti. Chizmalar mavzuni tushuntirish uchun soddalashtirilgan. Manbalar: https://modernrobotics.northwestern.edu/nu-gm-book-resource/9-1-and-9-2-point-to-point-trajectories-part-1-of-2/
https://www.universal-robots.com/manuals/EN/HTML/SW10_10/Content/prod-scriptmanual/all_scripts/movej_qa14v105t0r.htm
https://www.universal-robots.com/manuals/EN/HTML/SW5_19/Content/prod-usr-man/complianceUR16e/SW_sections/first_program/move.htm

## Slide 7
ROBOTOTEXNIKA / POZITSION BOSHQARUV
Nuqtadan nuqtaga harakat (PTP)
Robotlarning dasturiy boshqaruv tizimlari
07 / 15
01
Dasturchi robot qayerdan qayerga borishini belgilaydi.
02
Kontroller berilgan tezlik va tezlanish chegaralariga mos harakatni hisoblaydi.
03
Bo‘g‘imlar birgalikda ishlaydi. Asbob nuqtalar orasida egri yo‘l bo‘ylab ham yurishi mumkin.
A
B
Ko‘k: shartli asbob yo‘li
Kulrang: A va B orasidagi kesma
Notes: O‘quv taqdimoti. Chizmalar mavzuni tushuntirish uchun soddalashtirilgan. Manbalar: https://modernrobotics.northwestern.edu/nu-gm-book-resource/9-1-and-9-2-point-to-point-trajectories-part-1-of-2/
https://www.universal-robots.com/manuals/EN/HTML/SW10_10/Content/prod-scriptmanual/all_scripts/movej_qa14v105t0r.htm
https://www.universal-robots.com/manuals/EN/HTML/SW5_19/Content/prod-usr-man/complianceUR16e/SW_sections/first_program/move.htm

## Slide 8
ROBOTOTEXNIKA / POZITSION BOSHQARUV
Bitta o‘qning teskari aloqa konturi
Robotlarning dasturiy boshqaruv tizimlari
08 / 15
Topshiriq
q*
Xatolik
e = q* − q
Regulyator
Motor va
bo‘g‘im
Enkoder o‘lchagan haqiqiy holat q
Datchik holatni o‘lchaydi. Kontroller topshiriq bilan farqni solishtirib, motor ishini tuzatadi.
Notes: O‘quv taqdimoti. Chizmalar mavzuni tushuntirish uchun soddalashtirilgan. Manbalar: https://modernrobotics.northwestern.edu/nu-gm-book-resource/9-1-and-9-2-point-to-point-trajectories-part-1-of-2/
https://www.universal-robots.com/manuals/EN/HTML/SW10_10/Content/prod-scriptmanual/all_scripts/movej_qa14v105t0r.htm
https://www.universal-robots.com/manuals/EN/HTML/SW5_19/Content/prod-usr-man/complianceUR16e/SW_sections/first_program/move.htm

## Slide 9
ROBOTOTEXNIKA / POZITSION BOSHQARUV
Harakatning tezlik profili
Robotlarning dasturiy boshqaruv tizimlari
09 / 15
Trapesiyasimon profil
v
t
Tezlanish
Bir tekis yurish
Sekinlashish
Cheklovlar
Maksimal tezlik
Maksimal tezlanish
Bo‘g‘im chegaralari
Qisqa siljishda doimiy tezlik qismi bo‘lmasligi mumkin.
Notes: O‘quv taqdimoti. Chizmalar mavzuni tushuntirish uchun soddalashtirilgan. Manbalar: https://modernrobotics.northwestern.edu/nu-gm-book-resource/9-1-and-9-2-point-to-point-trajectories-part-1-of-2/
https://www.universal-robots.com/manuals/EN/HTML/SW10_10/Content/prod-scriptmanual/all_scripts/movej_qa14v105t0r.htm
https://www.universal-robots.com/manuals/EN/HTML/SW5_19/Content/prod-usr-man/complianceUR16e/SW_sections/first_program/move.htm

## Slide 10
ROBOTOTEXNIKA / POZITSION BOSHQARUV
Dastur bajarilish algoritmi
Robotlarning dasturiy boshqaruv tizimlari
10 / 15
1. Boshlang‘ich tekshiruv
2. Navbatdagi pozitsiyani o‘qish
3. Harakatni bajarish
4. Yetishni tasdiqlash
5. Texnologik amal
6. Keyingi bosqich
Tasdiq signali belgilangan vaqtda kelmasa, kontroller xatoni qayd etadi.
Notes: O‘quv taqdimoti. Chizmalar mavzuni tushuntirish uchun soddalashtirilgan. Manbalar: https://modernrobotics.northwestern.edu/nu-gm-book-resource/9-1-and-9-2-point-to-point-trajectories-part-1-of-2/
https://www.universal-robots.com/manuals/EN/HTML/SW10_10/Content/prod-scriptmanual/all_scripts/movej_qa14v105t0r.htm
https://www.universal-robots.com/manuals/EN/HTML/SW5_19/Content/prod-usr-man/complianceUR16e/SW_sections/first_program/move.htm

## Slide 11
ROBOTOTEXNIKA / POZITSION BOSHQARUV
Detalni olib qo‘yish sikli
Robotlarning dasturiy boshqaruv tizimlari
11 / 15
P0: kutish
P1: detal tepasiga kelish
P2: tushish va ushlash
P3: ko‘tarish
P4: qo‘yish joyiga kelish
P5: tushish va bo‘shatish
P1
P2
P4
P5
Olish joyi
Qo‘yish joyi
Soddalashtirilgan ko‘chirish sxemasi
Notes: O‘quv taqdimoti. Chizmalar mavzuni tushuntirish uchun soddalashtirilgan. Manbalar: https://modernrobotics.northwestern.edu/nu-gm-book-resource/9-1-and-9-2-point-to-point-trajectories-part-1-of-2/
https://www.universal-robots.com/manuals/EN/HTML/SW10_10/Content/prod-scriptmanual/all_scripts/movej_qa14v105t0r.htm
https://www.universal-robots.com/manuals/EN/HTML/SW5_19/Content/prod-usr-man/complianceUR16e/SW_sections/first_program/move.htm

## Slide 12
ROBOTOTEXNIKA / POZITSION BOSHQARUV
Dastur namunasi va blokirovkalar
Robotlarning dasturiy boshqaruv tizimlari
12 / 15
Shartli psevdokod
01 WAIT detal_bor
02 MOVE P1
03 MOVE P2
04 CLOSE qisqich
05 WAIT detal_ushlandi
06 MOVE P3
07 MOVE P4
08 MOVE P5
09 OPEN qisqich
10 MOVE P0
Keyingi amal qachon boshlanadi?
Detal mavjudligi
Qisqichning tasdiq signali
Maqsad pozitsiyaga yetish
Kutish vaqtining chegarasi
Buyruqlar o‘quv misoli. Aniq sintaksis kontrollerga bog‘liq.
Notes: O‘quv taqdimoti. Chizmalar mavzuni tushuntirish uchun soddalashtirilgan. Manbalar: https://modernrobotics.northwestern.edu/nu-gm-book-resource/9-1-and-9-2-point-to-point-trajectories-part-1-of-2/
https://www.universal-robots.com/manuals/EN/HTML/SW10_10/Content/prod-scriptmanual/all_scripts/movej_qa14v105t0r.htm
https://www.universal-robots.com/manuals/EN/HTML/SW5_19/Content/prod-usr-man/complianceUR16e/SW_sections/first_program/move.htm

## Slide 13
ROBOTOTEXNIKA / POZITSION BOSHQARUV
Dasturlash va sozlash
Robotlarning dasturiy boshqaruv tizimlari
13 / 15
01
Operator robotni kerakli holatga olib keladi va shu pozitsiyani xotiraga yozadi.
02
Dasturda nuqtalar tartibi, harakat tezligi va qisqich buyruqlari belgilanadi.
03
Sinov paytida koordinatalar, asbob o‘lchami va ko‘tariladigan yuk tekshiriladi.
1. Nuqtalarni yozish
2. Ketma-ketlik tuzish
3. Past tezlikda sinash
Notes: O‘quv taqdimoti. Chizmalar mavzuni tushuntirish uchun soddalashtirilgan. Manbalar: https://modernrobotics.northwestern.edu/nu-gm-book-resource/9-1-and-9-2-point-to-point-trajectories-part-1-of-2/
https://www.universal-robots.com/manuals/EN/HTML/SW10_10/Content/prod-scriptmanual/all_scripts/movej_qa14v105t0r.htm
https://www.universal-robots.com/manuals/EN/HTML/SW5_19/Content/prod-usr-man/complianceUR16e/SW_sections/first_program/move.htm

## Slide 14
ROBOTOTEXNIKA / POZITSION BOSHQARUV
Afzalliklar va cheklovlar
Robotlarning dasturiy boshqaruv tizimlari
14 / 15
Afzalliklar
Bir xil amallarni ko‘p marta takrorlashga mos.
Ish nuqtalarini yozish va keyin o‘zgartirish qulay.
Detalni ko‘chirish va dastgohga yuklashda qo‘llanadi.
Cheklovlar
Nuqtalar orasidagi yo‘lda to‘siq yo‘qligini tekshirish kerak.
Chok yoki kesish yo‘lini aniq kuzatish uchun kontur boshqaruvi kerak.
Aniqlikka sozlash sifati, yuk va mexanizmdagi bo‘shliqlar ta’sir qiladi.
Notes: O‘quv taqdimoti. Chizmalar mavzuni tushuntirish uchun soddalashtirilgan. Manbalar: https://modernrobotics.northwestern.edu/nu-gm-book-resource/9-1-and-9-2-point-to-point-trajectories-part-1-of-2/
https://www.universal-robots.com/manuals/EN/HTML/SW10_10/Content/prod-scriptmanual/all_scripts/movej_qa14v105t0r.htm
https://www.universal-robots.com/manuals/EN/HTML/SW5_19/Content/prod-usr-man/complianceUR16e/SW_sections/first_program/move.htm

## Slide 15
ROBOTOTEXNIKA / POZITSION BOSHQARUV
Xulosa
Robotlarning dasturiy boshqaruv tizimlari
15 / 15
Robotning ish sikli dasturda saqlangan nuqtalar va amallar ketma-ketligidan tuziladi.
Har bir bosqichda pozitsiya va datchik signallarini tekshirish siklning to‘g‘ri bajarilishini ta’minlaydi.
Manbalar
1. K. Lynch, F. Park. Modern Robotics, 9.1–9.2: Point-to-Point Trajectories.
2. Universal Robots. URScript: movej buyrug‘i va harakat parametrlari.
3. Universal Robots. Basic Program Nodes: MoveJ va MoveL.
Notes: To‘liq manbalar:
https://modernrobotics.northwestern.edu/nu-gm-book-resource/9-1-and-9-2-point-to-point-trajectories-part-1-of-2/
https://www.universal-robots.com/manuals/EN/HTML/SW10_10/Content/prod-scriptmanual/all_scripts/movej_qa14v105t0r.htm
https://www.universal-robots.com/manuals/EN/HTML/SW5_19/Content/prod-usr-man/complianceUR16e/SW_sections/first_program/move.htm